## Slide 1: DS3105 Computer Networking
Stop and wait ARQ Protocol
T.Kayalvizhy

## Slide 2: Learning Objectives
Learning Outcome | Description
ILO 01 | Demonstrate knowledge & Understand of operation of wireless networks, Emerging topics in computer networks, range of network architectures & protocols

## Slide 3: What is a Wireless Network?
A wireless network allows devices to communicate without physical cables, using radio waves, infrared, or microwave signals.
Common examples: Wi-Fi, Bluetooth, Cellular (4G/5G), Satellite.
Works through transmitters, receivers, and antennas.
Flexibility & mobility: users can connect anytime, anywhere.

## Slide 4: Features and Challenges of Wireless Communication
Main Features:
  Mobility: users can move freely while connected.
  Ease of deployment: no physical cabling needed.
  Scalability: easy to add new devices.
Challenges:
  Interference: radio signals overlap or distort.
  Limited bandwidth: shared medium → congestion.
  Signal fading: obstacles weaken signal strength.
  Security threats: easier eavesdropping than wired networks.

## Slide 5: Errors in Data Transmission
In wireless communication, data travels through the air, not cables.
The wireless medium is unpredictable signals are affected by:
  Noise and interference (from other devices)
  Obstacles and signal fading
  Mobility of users (changing distance, handoffs)
  Atmospheric conditions

## Slide 6: Errors in Data Transmission
Result:
Bits may get flipped, lost, or duplicated during transmission.
Leads to errors in received data.
Example:
  Sent: 11001010 → Received: 11011010 (1 bit error)

## Slide 7: Ensuring Reliable Wireless Communication
Wireless networks can’t guarantee perfect delivery, so reliability must come from the software/protocol level.
Error control techniques help:
  Detect errors caused by channel noise or interference.
  Correct or retransmit corrupted data automatically.
  Maintain Quality of Service (QoS) for applications like video calls, IoT, etc.

## Slide 8: Two Main Approaches
Technique | Method | Example | Use Case
ARQ (Automatic Repeat Request) | Detect errors (request retransmission) | Stop-and-Wait, Go-Back-N, Selective Repeat | Reliable but increases the delay, simpler, but needs acknowledgment
FEC (Forward Error Correction) | Add redundant bits (correct errors at the receiver) | Hamming Code, Reed–Solomon | Used in real-time & noisy channels, faster (no retransmission), but uses more bandwidth.

## Slide 9: Stop and wait ARQ Protocol
The stop-and-wait protocol is a data link layer protocol for the transmission of frames over noiseless channels.
It provides unidirectional data transmission with flow control facilities but without error control facilities.
After transmitting one frame, the sender waits for an acknowledgement before transmitting the next frame.
Stop and wait ARQ =Stop and wait + Timeout timer +Sequence number.

## Slide 10: Stop and wait ARQ Protocol
Sender side:
  Send one data packet at a time.
  Send the next packet only after receiving an ACK for the previous.
Receiver side:
  Receive and consume data packet.
  After consuming the packet, ACK need to be sent(Flow Control).
Sender
Receiver
Frame
ACK
Time
Timeout
The ACK is received before the timer expires.

## Slide 11: Problems of Stop and wait Protocol
Problems due to lost data
  Sender waits for an ack for an infinite amount of time.
  Receiver waits for data for an infinite amount of time.
Sender
Receiver
Frame
The Original frame is lost

## Slide 12: Problems of Stop and wait Protocol
Problems due to lost ACK.
  Sender waits for an infinite amount of time for ack.
Sender
Receiver
Frame
ACK
Time
Timeout
The ACK is lost.

## Slide 13: Problems of Stop and wait Protocol
Problems due to delayed ACK/data.
  After a timeout on the sender side, a delayed ack might be wrongly considered as an ack of some other data packet.
Sender
Receiver
Frame
ACK
Time
Timeout
The timeout fires too soon.
Frame
ACK

## Slide 14: What is Hamming Code?
A Forward Error Correction (FEC) technique developed by Richard Hamming (1950).
Adds extra parity bits to data bits → allows single-bit error detection and correction.
Redundancy is added so the receiver can find and correct one wrong bit without retransmission.
Used in: memory systems, digital communication, satellite links, etc.

## Slide 15: Hamming Code
Insert parity bits at positions that are powers of 2Example: positions 1, 2, 4, 8, …Each parity bit covers specific data bits. Helps locate the error bit position directly. Formula: For m data bits and r parity bits:
Hamming Code=(n, r) where n=m + r

## Slide 16: Hamming Code Example
Data bits (original): 01101
Received codeword: 001101110
Determine how many parity bits are used in this Hamming Code.
Identify the positions of the parity bits and data bits in the received code.
Perform parity checking to find the syndrome bits.
Determine the position of the error (if any).
Correct the error and write the corrected codeword.
Extract the original data bits after correction.

## Slide 17: Thank you
Any Questions?